## Slide 1
Robert H. Dodds, Jr., PhD, NAE
Periodic Boundary Conditions for 3D Representative Volume Element Models:
Theory and Implementation in WARP3D
University of Illinois at Urbana-Champaign
cee.illinois.edu/directory/profile/rdodds
rhdodds@gmail.com
Last revision: December 26, 2025
WARP3D input files available upon request

## Slide 2: RVEs and PBCs
3D RVE meshed with finite elements
Strain tensor computed for example at integration points of the macroscale finite element model
Periodic part of the total displacement field. Must be identical at matching points (node pairs) on (+,-) surfaces, e.g., (+,-) x faces as marked
One of first to employ this notation:
P.M. Suquet. Elements of homogenization for inelastic solid mechanics. In Homogenization Techniques for Composite Media. Edited by Sanchez-Palencia and A. Zaoui). Lecture Notes in Physics, 272, 1987.
A
Periodic part

## Slide 3: Other References
Journal of Engineering Materials and Technology, Vol. 136, 011007-1:011007-16, 2014. doi.org/10.1115/1.4025916.

## Slide 4: Common Case: Rectangular Prisms
RVE meshed with “pair nodes” to support application of periodic boundary conditions.
Pairs of nodes located on opposite faces of the RVE whose in-plane coordinates are identical. They represent the same physical point in the periodic material and are coupled by the periodic displacement constraints. GMSH and NEPER, for example, can generate RVE meshes with the required pair nodes.
Node sets:
Vertex nodes: A B C D E F G H
Edge nodes: along the 12 edges excluding the vertex nodes
Face nodes: incident on faces, excluding vertex and edge nodes
Internal nodes: all other mesh nodes

## Slide 5: Macroscale Strain to Load RVE
Developments here for multi-point constraint (MPC) equations to enforce the PBCs assume, but do not require, a symmetric strain tensor in the above equation.
Known macroscale strain tensor to load the RVE

## Slide 6: 3D PBCs (see A on pg. 2)
The RVE does not need to be located in the 1st quadrant with node A at (0,0,0)
Reduction to the 2D case is straightforward (vertexes H-G-D-C deleted)

## Slide 7: Multi-Point Constraint Equations
The PBCs are multi-point constraint (MPC) equations.
When the known, (loading) strain terms in an equation are zero, the MPC is homogeneous.
When one or more of the known (loading) strain terms is not zero, the MPC is inhomogeneous.
Some finite element codes, including WARP3D, support only homogeneous MPC equations.
The dummy node – rigid link technique is often used to overcome this limitation.
constraints
14 u = 0 v = 0
642 u = 0.1 w = -0.3
…
…
multipoint
23 1.0 v - 5 1.0 v = 0.
23 1.0 w - 5 1.0 w = 0.
18 1.0 u - 10 1.0 u - 28 1.0 u = 0.
18 1.0 v - 10 1.0 v = 0.
18 1.0 w - 10 1.0 w = 0.
12 1.0 u - 16 1.0 u - 28 1.0 u = 0.
12 1.0 v - 16 1.0 v = 0.
…
…
WARP3D input format
The “absolute” constraint must come first.
The keyword “multipoint” ends the absolute constraints and starts the MPCs.
No absolute constraints can be mixed with the multipoint constraints.
Every MPC equation must be homogeneous.
No coefficient in an MPC equation may = 0.
Coefficients can be other than 1.0.
If the ”constraints” command appears again in the input, *all* existing constraint definition are deleted.

## Slide 8: Dummy Node – Link Element Technique
Link element has 2 nodes, most often with identical coordinates – coordinates play no role in the element stiffness matrix (only connectivity and stiffness values matter).
Placed away from RVE mesh for clarity but location has no effect on solution.
Nodes connected by stiff, linear springs oriented along global X-Y-Z axes
Connected to nodes 49, 50 in figure.
In this example, displacements are applied to node 50 with node 49 appearing in the MPC equations.
With sufficiently large spring stiffnesses, node 49 displacements are identical to those imposed at node 50.
But, the MPC equations written using node 49 satisfy the requirement to be homogeneous.
Node 49 is often termed the “dummy” node
Remember: in WARP3D the nodes must be numbered sequentially and the elements must be numbered sequentially. The dummy nodes and link elements are generally added after model nodes/elements.

## Slide 9: Example: Dummy Node – Link Element
Example MPC equation using the dummy node 49 (WARP3D format):
Where absolute constraints are imposed on node 50 (WARP3D format): The u = v = 0 displacements on node 50 have no effect on the solution unless they appear in other MPC equations having node 49. For WARP3D, do not include terms in MPCs with a zero multiplier, e.g. 49 0.0 w

## Slide 10: Verification Example
Rectangular prism RVE
8, 8-node elements (l3disop)
4 link2 elements
27 nodes for prism
4 dummy-node pairs (8 total nodes)
Lx = 1, Ly = 2, Lz = 4
Linear-elastic material
Confirm correct MPCs w/dummy nodes to enforce PBCs
Vertex
Edge
Face
Internal
A 1
B 3
C 21
D 19
E 7
F 9
G 27
H 25
FG 18
AD 10
HG 26
AB 2
GC 24
EA 14
BC 12
EH 16
FE 8
CD 20
FB 6
HD 22
EHDA 13
FGCB 15
BADC 11
FEHG 17
FEAB 15
GHDC 23
14
Node Sets
(A node can appear only once)
In more refined meshes, there will be many nodes on each edge, each face and internal to the RVE

## Slide 11: Mesh Data
Coordinates
Incidences
1 1 2 5 4 10 11 14 13
2 2 3 6 5 11 12 15 14
3 4 5 8 7 13 14 17 16
4 5 6 9 8 14 15 18 17
5 10 11 14 13 19 20 23 22
6 11 12 15 14 20 21 24 23
7 13 14 17 16 22 23 26 25
14 15 18 17 23 24 27 26
28 29
30 31
32 33
34 35
1 0.0 0.0 0.0
2 0.5 0.0 0.0
3 1.0 0.0 0.0
4 0.0 1.0 0.0
5 0.5 1.0 0.0
6 1.0 1.0 0.0
7 0.0 2.0 0.0
8 0.5 2.0 0.0
9 1.0 2.0 0.0
10 0.0 0.0 2.0
11 0.5 0.0 2.0
12 1.0 0.0 2.0
13 0.0 1.0 2.0
14 0.5 1.0 2.0
15 1.0 1.0 2.0
16 0.0 2.0 2.0
17 0.5 2.0 2.0
18 1.0 2.0 2.0
19 0.0 0.0 4.0
20 0.5 0.0 4.0
21 1.0 0.0 4.0
22 0.0 1.0 4.0
23 0.5 1.0 4.0
24 1.0 1.0 4.0
25 0.0 2.0 4.0
26 0.5 2.0 4.0
1.0 2.0 4.0
10 10 10
10 10 10
10 10 10
10 10 10
10 10 10
10 10 10
10 10 10
10 10 10
material steel
properties mises e 30000 nu 0.3 n_power 10 yld_pt 60.e10
!
material rve_link
properties link stiff_link 1.0e10 mass_link 0.0
!
elements
1-8 type l3disop linear material steel order 2x2x2 bbar,
center_output short
9-12 type link2 material rve_link
!
Link2 elements
Dummy nodes
Linear-elastic
Put coordinates and incidences into file name: coords_incid.inp

## Slide 12: Loadings, Dummy-Nodes
Numerical values specified for easy verification that computed results in all mesh elements are identical to these strains.
4 dummy-node pairs and 4 corresponding stiff link2 elements are defined to impose displacements on the RVE that correspond to these macroscale strains.
The RVE dimensions (1 x 2 x 4) are chosen to make clear the different displacement values required to impose specific macroscale strains
One dummy-node pair and link2 element for each strain component (here the macroscale shear strains are symmetric)
The (2,2) and (3,3) strain values could also be specified with non-zero values. Add 2 more dummy-node pairs and 2 link2 elements
Coordinates for nodes 28-35 are set at 10.0 10.0 10.0 . The values are immaterial and do not affect the solution.
link2 stiffnesses are set at 1010 – check that this value is sufficiently large to approximate a rigid-link
Dummy-Node Pairs Link2 element
28, 29 9
30, 31 10
32, 33 11
34, 35 12

## Slide 13: Simple loading: Only
All dummy-node pairs and link2 elements remain in model for convenience.
Absolute displacements imposed:
u = 0.1 at node 29 makes u at node 28 = 0.1
The u = 0.1 makes macroscale strain 𝜀11 = 0.1 since Lx = 1.0: 𝜀11 = u29 = u28/1.0
Recommended steps:
  Decide upon absolute constraints to prevent 3 rigid body translations and 3 rotations (rigid-body constraints).
  Start with all equations on slide 6. Eliminate all the terms that become zero from the zero imposed 𝜀ij values.
  Eliminate the terms that become zero from the rigid-body constraints.
  Some of the MPCs to enforce the periodic boundary conditions will now have only 1 term remaining.
  The MPC has become an absolute constraint and must be included with them.
Remove rigid-body motions:
Node 1: u = v = w = 0
Node 3: v = w = 0
Node 7: w = 0
(other combinations will work as well)
Impose dummy-node loading:
Node 29 : u = 0.1, v = w = 0
Periodic MPCs that become absolute constraints:
Node 21 : w = 0
Node 25 : v = 0 w = 0
Node 27 : v = 0 w = 0
What about dummy nodes 30-35?
No constraints needed but can be set = 0 if desired. Nodes 29-35 do not appear in any MPCs for this simple loading with only 𝜀11 non-zero. The stiff springs of the link elements 10, 11, 12 effectively attach them to ground - and they have no applied loads so zero displacements are computed.
Solution: all elements for this uniformly meshed RVE must have 𝜀11 = 0.1 and other strains = 0

## Slide 14: MPCs to Enforce Periodic Boundary
15 1.0 u - 13 1.0 u - 28 1.0 u = 0.
15 1.0 v - 13 1.0 v = 0.
15 1.0 w - 13 1.0 w = 0.
17 1.0 u - 11 1.0 u = 0.
17 1.0 v - 11 1.0 v = 0.
17 1.0 w - 11 1.0 w = 0.
23 1.0 u - 5 1.0 u = 0.
23 1.0 v - 5 1.0 v = 0.
23 1.0 w - 5 1.0 w = 0.
18 1.0 u - 10 1.0 u - 28 1.0 u = 0.
18 1.0 v - 10 1.0 v = 0.
18 1.0 w - 10 1.0 w = 0.
12 1.0 u - 16 1.0 u - 28 1.0 u = 0.
12 1.0 v - 16 1.0 v = 0.
12 1.0 w - 16 1.0 w = 0.
24 1.0 u - 4 1.0 u - 28 1.0 u = 0.
24 1.0 v - 4 1.0 v = 0.
24 1.0 w - 4 1.0 w = 0.
6 1.0 u - 22 1.0 u - 28 1.0 u = 0.
6 1.0 v - 22 1.0 v = 0.
6 1.0 w - 22 1.0 w = 0.
26 1.0 u - 2 1.0 u = 0.
26 1.0 v - 2 1.0 v = 0.
26 1.0 w - 2 1.0 w = 0.
8 1.0 u - 20 1.0 u = 0.
8 1.0 v - 20 1.0 v = 0.
8 1.0 w - 20 1.0 w = 0.
27 1.0 u - 28 1.0 u = 0.
9 1.0 u - 19 1.0 u - 28 1.0 u = 0.
9 1.0 v - 19 1.0 v = 0.
9 1.0 w - 19 1.0 w = 0.
25 1.0 u - 3 1.0 u + 28 1.0 u = 0.
21 1.0 u - 7 1.0 u - 28 1.0 u = 0.
21 1.0 v - 7 1.0 v = 0.
Multipoint
Put multipoint constraints into file name: mpc_eps_11_loading.inp
𝜀11 = 0.1, all other macroscale strains = 0

## Slide 15: Complete Input File (1)
!
! 3D rectangular prism RVE. Lx = 1, Ly = 2, Lz = 4
!
! Periodic boundary conditions (PBCs) applied to enforce the
! RVE macroscale strain tensor:
!
! 0.1 0.0 0.0 # eps_xx, eps_xy, eps_xz alternate notation: eps_11, eps_12, eps_13
! 0.0 0.0 0.0 # eps_xy, eps_yy, eps_yz
! 0.0 0.0 0.0 # eps_xz, eps_yz, eps_zz
!
!
material steel
properties mises e 30000 nu 0.3 n_power 10 yld_pt 60.e10 $ linear-elastic
!
material rve_link
properties link stiff_link 1.0e10 mass_link 0.0
!
structure prism
!
number of nodes 35 elements 12
!
elements
1-8 type l3disop linear material steel order 2x2x2 bbar,
center_output short
9 10 11 12 type link2 material rve_link
!
*echo off
*input from file "coords_incid.inp"
*echo on
!

## Slide 16: Complete Input File (2)
blocking automatic
!
constraints
!
1 u 0.0 v 0.0 w 0.0 $ on nodes 1,3, 7 to prevent rigid motions
3 v 0.0 w 0.0
7 w 0.0
21 w 0.0 $ on 21, 25, 27 as a result on MPCs becoming absolutes
25 v 0.0 w 0.0
27 v 0.0 w 0.0
29 u 0.1 $ eps_11 strain
!
*input from file "mpc_eps_11_loading.inp"
!
loading test
nonlinear
step 1 constraints 1.0
!
nonlinear analysis parameters $ only those really needed here
solution technique sparse direct
time step 1.0e06
maximum iterations 5 $ global Newton iterations
minimum iterations 1
convergence test norm res tol 0.001
batch messages off
trace solution on
!
output model flat patran convention text file "model"
!
compute displacements for loading test step 1
output wide strains 1-8
output wide stresses 1-12
output wide displacements 1-35
output flat text displacements $ for ParaView visualization
output flat text element stresses $ for ParaView visualization
!
stop
For use by ParaView

## Slide 17: More Complete Loading
All dummy-node pairs and link2 elements in the model.
Absolute displacements imposed on dummy nodes = macroscale strains.
Recommended steps:
  Decide upon absolute constraints to prevent 3 rigid body translations and 3 rotations (rigid-body constraints).
  Start with all equations on slide 6. Eliminate all the terms that become zero from the zero imposed 𝜀ij values.
  Eliminate the terms that become zero from the rigid-body constraints.
  Some of the MPCs to enforce the periodic boundary conditions will now have only 1 term remaining.
  The MPC has become an absolute constraint and must be included with them.
Remove rigid-body motions:**
Node 1: u = v = w = 0
Impose dummy-node loading:
Node 29 : u = 0.1, v = w = 0 ← 𝜀11
Node 31 : u = 0.2, v = 0.2, w = 0 ← 𝜀12 = 𝜀21
Node 33 : u = 0.5, v = 0.0, w = 0.5 ← 𝜀13 = 𝜀31
Node 35 : u = 0.0, v = 0.3, w = 0.3 ← 𝜀23 = 𝜀32
Periodic MPCs that become absolute constraints:
*** none ***
Solution: all elements for this uniformly meshed RVE must have the imposed macroscale strain tensor
Macroscale tensor
** For this loading, there are sufficient non-zero imposed displacements (from the macroscale strain tensor) to suppress rigid-body rotations

## Slide 18: MPCs to Enforce Periodic Boundary
Multipoint
Put multipoint constraints into file name: mpc_eps_all_loading.inp
15 1.0 u - 13 1.0 u - 28 1.0 u = 0.
15 1.0 v - 13 1.0 v - 30 1.0 v = 0.
15 1.0 w - 13 1.0 w - 32 1.0 w = 0.
17 1.0 u - 11 1.0 u - 30 2.0 u = 0.
17 1.0 v - 11 1.0 v = 0.
17 1.0 w - 11 1.0 w - 34 2.0 w = 0.
23 1.0 u - 5 1.0 u - 32 4.0 u = 0.
23 1.0 v - 5 1.0 v - 34 4.0 v = 0.
23 1.0 w - 5 1.0 w = 0.
18 1.0 u - 10 1.0 u - 28 1.0 u - 30 2.0 u = 0.
18 1.0 v - 10 1.0 v - 30 1.0 v = 0.
18 1.0 w - 10 1.0 w - 32 1.0 w - 34 2.0 w = 0.
12 1.0 u - 16 1.0 u - 28 1.0 u + 30 2.0 u = 0.
12 1.0 v - 16 1.0 v - 30 1.0 v = 0.
12 1.0 w - 16 1.0 w - 32 1.0 w + 34 2.0 w = 0.
24 1.0 u - 4 1.0 u - 28 1.0 u - 32 4.0 u = 0.
24 1.0 v - 4 1.0 v - 30 1.0 v - 34 4.0 v = 0.
24 1.0 w - 4 1.0 w - 32 1.0 w = 0.
6 1.0 u - 22 1.0 u - 28 1.0 u + 32 4.0 u = 0.
6 1.0 v - 22 1.0 v - 30 1.0 v + 34 4.0 v = 0.
6 1.0 w - 22 1.0 w - 32 1.0 w = 0.
26 1.0 u - 2 1.0 u - 30 2.0 u - 32 4.0 u = 0.
26 1.0 v - 2 1.0 v - 34 4.0 v = 0.
26 1.0 w - 2 1.0 w - 34 2.0 w = 0.
8 1.0 u - 20 1.0 u - 30 2.0 u + 32 4.0 u = 0.
8 1.0 v - 20 1.0 v + 34 4.0 v = 0.
8 1.0 w - 20 1.0 w - 34 2.0 w = 0.
27 1.0 u - 28 1.0 u - 30 2.0 u - 32 4.0 u = 0.
27 1.0 v - 30 1.0 v - 34 4.0 v = 0.
27 1.0 w - 32 1.0 w - 34 2.0 w = 0.
9 1.0 u - 19 1.0 u - 28 1.0 u - 30 2.0 u + 32 4.0 u = 0.
9 1.0 v - 19 1.0 v - 30 1.0 v + 34 4.0 v = 0.
9 1.0 w - 19 1.0 w - 32 1.0 w - 34 2.0 w = 0.
25 1.0 u - 3 1.0 u + 28 1.0 u - 30 2.0 u - 32 4.0 u = 0.
25 1.0 v - 3 1.0 v + 30 1.0 v - 34 4.0 v = 0.
25 1.0 w - 3 1.0 w + 32 1.0 w - 34 2.0 w = 0.
21 1.0 u - 7 1.0 u - 28 1.0 u + 30 2.0 u - 32 4.0 u = 0.
21 1.0 v - 7 1.0 v - 30 1.0 v - 34 4.0 v = 0.
21 1.0 w - 7 1.0 w - 32 1.0 w + 34 2.0 w = 0.
The Lx, Ly, Lz values apparent here

## Slide 19: Complete Input File (1)
!
! 3D rectangular prism RVE. Lx = 1, Ly = 2, Lz = 4
!
! Periodic boundary conditions (PBCs) applied to enforce the
! RVE macroscale strain tensor:
!
! 0.1 0.2 0.5 # eps_xx, eps_xy, eps_xz alternate notation: eps_11, eps_12, eps_13
! 0.2 0.0 0.3 # eps_xy, eps_yy, eps_yz
! 0.5 0.3 0.0
!
! ***** Note *****
!
! WARP3D outputs the engineering definition of shear strains, i.e.,
! gamma_xy, gamma_yz, gamma_xz
! The printed results should thus be gamma_xy = 0.4,
! gamma_yz = 0.6 and gamma_xz = 1.0
!
material steel
properties mises e 30000 nu 0.3 n_power 10 yld_pt 60.e10 $ linear-elastic
!
material rve_link
properties link stiff_link 1.0e10 mass_link 0.0
!
structure prism
!
number of nodes 35 elements 12
!
elements
1-8 type l3disop linear material steel order 2x2x2 bbar,
center_output short
9 10 11 12 type link2 material rve_link
!
*echo off
*input from file "coords_incid.inp"
*echo on
!

## Slide 20: Complete Input File (2)
blocking automatic
!
constraints
!
1 u 0.0 v 0.0 w 0.0 $ non-zero displacements on dummy nodes are
! $ sufficient to prevent rigid rotations
!
! set node 29 u = eps_11 value
! set node 31 u, v = eps_12 value
! set node 33 u, w = eps_13 value
! set node 35 u, w = eps_23 value
!
29 u 0.1 v 0.0 w 0.0
31 u 0.2 v 0.2 w 0.0
33 u 0.5 v 0.0 w 0.5
35 u 0.0 v 0.3 w 0.3
!
multipoint
!
*input from "mpc_eps_all_loading.inp"
!
loading test
nonlinear
step 1 constraints 1.0
<<<< remainder of file same as eps_11 only loading >>>>

## Slide 21: Program to Make MPCs
The simple example here makes clear that many thousands of MPC equations are needed to enforce the PBCs for RVEs with many elements
A Python program, rve_mpc_generator.py, is available in the RVE_support directory of the WAR3D distribution
Uses a small text input file of commands and the RVE nodal coordinates to generate a file of ready-to-use constraint data in WARP3D format
The short manual for the program is named manual.pdf in the RVE_support directory.